## Slide 1: Mission State Machine design for Image Based Follow-Me Drone
John Erickson
10/18/2015

## Slide 2: Outline
Mission State Machine diagram
Mission state descriptions
  State 0: Startup
  State 1: Target Acquisition
  State 2: Target Lock
  State 3: Mission Complete
Definitions

## Slide 3: Mission State Machine
Startup
Target Acquisition
Target
Lock
Mission Complete
Startup Success
Acquisition Success
End Mission
0
1
2
3
Startup Fail
Target Lost
Acquisition Fail

## Slide 4: State 0: Startup
Entry:
  Drone powered on
  Operator commands startup in Client application
Actions:
  Initialize Client application
  Client connects to Drone
  Client commands Drone take-off (operator input)
Exit:
  If startup successful, proceed to Target Acquisition state
  Else proceed to Mission Complete state

## Slide 5: State 1: Target Acquisition
Entry:
  Startup successfully completed OR
  Target Lost
Actions:
  Orient Drone for Target acquisition
  Acquire Target
    Maintain timer for acquisition timeout
    If needed, Yaw in place up to 360 degrees
    If needed, Yaw in outward spiral up to configuration limit
Exit:
  If Target acquired, proceed to Target Lock state
  Else proceed to Mission Complete state

## Slide 6: State 2: Target Lock
Entry:
  Target acquired
Actions:
  Client commands drone to desired orientation WRT Target
  Drone maintains relative orientation with mobile Target
Exit:
  If Target lost, proceed to Target Acquisition state
  If end mission command received, proceed to Mission Complete state

## Slide 7: State 3: Mission Complete
Entry:
  Startup failure OR
  Acquisition failure OR
  End mission command received
Actions:
  Command Drone to land
Exit:
  Drone powered off

## Slide 8: Definitions
Drone:
  AR.Drone 2.0 quadcopter
Client:
  Application running on laptop or Android phone
Target:
  Mobile object drone expected to track